Open On-Chip Debugger
Dominic Rath
University of Applied Sciences Augsburg

---
Content
JTAG
  - Overview, Uses
ARM Debugging
  - ARM Cores
  - ARM9TDMI
OpenOCD
  - Architecture
  - Supported JTAG Interfaces and Cores
Future Development

---
JTAG
IEEE 1149.1-2001
IEEE Standard Test Access Port and Boundary-Scan Architecture
Testing component functionality, connection, and interaction
-> TDI ->
-> TMS ->
-> TCK ->
<- TDO <-
TAP
bus
master
Device
under test #1
Device
under test #2

---
JTAG
TAP Statemachine
Test-Logic Reset	(TLR)
Run-Test/Idle	(RTI)
Select-DR-Scan	(SDS)
Capture-DR	(CD)
Shift-DR	(SD)
Exit1-DR	(E1D)
Pause-DR	(PD)
Exit2-DR	(E2D)
Update-DR	(UD)
Select-IR-Scan	(SIS)
Capture-IR	(CI)
Shift-IR	(SI)
Exit1-IR	(E1I)
Pause-IR	(PI)
Exit2-IR	(E2I)
Update-IR	(UI)
TLR
RTI
SDS
RTI
SIS
CD
RTI
CI
SD
RTI
SI
E1D
RTI
E1I
PD
RTI
PI
E2D
RTI
E2I
UD
RTI
UI

---
JTAG
Boundary-Scan Testing
Serially apply test vectors to output pins
Capture data on input pins
Detect open/short circuits
Functional testing
TDI
TDO

---
JTAG
In-System Programming
Programmable Logic Devices
  - CPLDs, FPGAs
Popular description files:
  - Serial Vector Format (SVF, XSVF)
  - Standard Test and Programming Language (STAPL), Jedec Std. No 71
    - Loop programming
    - Procedure calls
    - Conditional execution

---
ARM
Cores
ARM7
  - ARM7TDMI(-S)
  - ARM720T
ARM9
  - ARM920T / ARM922T
  - ARM926EJ-S
  - ARM946E-S / ARM966E-S
ARM10
ARM11
ARM Cortex
Intel XScale
Philips LPC2xxx
Atmel AT91SAM7/9
Atmel AT91RM
Analog Devices ADUC7xxx
Samsung S3C24xx/34xx/44xx
Intel PXA, IXP, IOP
...

---
ARM
Architecture Variants
ARMv4
  - 31 registers (r0 - r15 + banked registers)
  - 6 program status registers (CPSR + 5 SPSR)
  - 7 core states (USR, FIQ, IRQ, SVC, ABT, UND, SYS)
  - ARM and Thumb mode (32 / 16 bit instructions)
  - Flat 32-bit address room
ARMv5
  - Additional Jazelle mode (Java), DSP instructions
  - BKPT instruction (saves one breakpoint unit)
ARMv4/v5 MMU / Caches
  - Translation Lookaside Buffer
  - ICache, DCache (only ARM9+)

---
ARM
ARM7/9 Debugging
Embedded-ICE
  - Scan chain 2
    - 32 bit data
    - 5 bit address
    - 1 bit read/write
Core Debug
  - Scan chain 1
    - 32 bit data
    - 32 bit instruction (ARM9 only)
    - Control bits
JTAG
Embedded-ICE
Core
Boundary-Scan
ARM7TDMI

---
ARM7/9
Embedded-ICE Unit
Debug request
Breakpoint / Watchpoint handling
Debug communications channel
  - Fast memory transfers, semihosting, logging
Watchpoint 0
address mask
Watchpoint 0
address value
Watchpoint 0
data mask
Watchpoint 0
data value
Watchpoint 0
control mask
Watchpoint 0
control value
Watchpoint 1
address mask
Debug control
Debug status
Debug comms
control
Debug comms
data
Watchpoint 1
address value
Watchpoint 1
data mask
Watchpoint 1
data value
Watchpoint 1
control mask
Watchpoint 1
control value

---
ARM7/9
Embedded-ICE Scan-Chain 2
nRead/Write
Address[4:0]
Data[31:0]
Writes to Embedded-ICE registers
Reads require two accesses
  - nRead/Write = 0, Address of register, Data = don't care
  - Pass through Update-DR
    - Register is read
  - Shift data out of Scan-Chain 2
    - Could do a write, or request data for next read

---
ARM7/9
ARM9TDMI Pipeline
Serially insert instruction into core (SC1)
  - LDR, STR, LDM, STM
Clock instruction through pipeline
Capture output, supply input
Model pipeline behaviour
  - Instruction cycle times, pipeline interlocks (RAW)
Fetch
Instruction
fetch
Decode
Decode
Reg. Read
Write
Reg. Write
Execute
ALU/Shift
Memory
Data Memory
Access

---
ARM7/9
ARM9TDMI Scan-Chain 1
ID[0:31]
SYSSPEED
WPTANDBKPT
DDEN
DD[31:0]
Harvard architecture
  - separate data and instruction bus
Sysspeed bit for system-speed instructions
WPTANDBKPT indicates simultaneous watchpoint and breakpoint break
DDEN indicates valid data on DD[31:0]

---
ARM7/9
Examining System State
Core registers can be accessed at debug speed
  - Core clocked from DCLK (TCK cycles in RTI)
Memory subsystem (RAM, ROM, MMIO) can't be accessed at debug speed
  - Leave debug state, resynchronize to MCLK
  - Execute instruction (LDR/STR/LDM/STM) at system speed
  - Reenter debug state

---
ARM7/9
Caches, MMU
ARM9 cores have separate data and instruction caches
  - Ensure cache coherency (Write through, invalidate Icache)
Preserve Cache state
Preserve TLB state
Allow accesses using both VMA and PA
  - Simulate page table walking

---
OpenOCD
Architecture
GDB
Telnet client
GDB Server
Telnet Server
GDB Server
  - source level debugging
Telnet Server
  - low-level tasks
    - flash writing
    - virtual address translation
    - ...
Target Abstraction (target.h)
Target specific code
JTAG Abstraction (jtag.h)
JTAG hardware driver
Wiggler, PLD cables, FT2232, ...
Target (ARM7/9 based uC)
JTAG

---
OpenOCD
CLI And Configuration
Target state manipulation
  - poll, halt, resume, step, reset
Memory access
  - md[bhw], mw[bhw]
  - load_binary
  - dump_binary
Breakpoint/Watchpoint handling
  - [r]bp, [r]wp
Flash handling
  - probe, erase, write, erase_check, protect_check
JTAG control
  - var, field
  - irscan, drscan, statemove, runtest, endstate, jtag_reset
Daemon operation
  - attach, reset
Reset modes
  - run, halt, init, run and halt
JTAG configuration
  - interface, jtag_device, reset_config, jtag_speed
Target configuration
  - arm7tdmi, arm9tdmi, arm720t, arm920t
Flash configuration
  - lpc2000, cfi

---
OpenOCD
Supported JTAG interfaces
Wiggler, PLD download cables
  - PC parallel port interfaces with level shifters
  - supported by generic bitbanging algorithm
FTDI FT2232
  - USB 2.0 full-speed with multi protocol synchronous serial engine (MPSSE)
    - may be operated as JTAG, SPI, ...
Amontec JTAG Accelerator (Chameleon)
  - Xilinx CPLD with EPP interface

---
OpenOCD
Open Source Toolchain
Eclipse IDE + Embedded CDT (Zylin.com)
GNU Toolchain
(gcc, binutils, ...)
OpenOCD
GDB
(through Eclipse)
ARM cross-
development with Eclipse by Jim Lynch (www.olimex.com/dev/arm-jtag/)

---
OpenOCD
Future Enhancements
Support for additional ARM7/9 cores
  - ARM9EJ-S (ARM926EJ-S)
Support for additional flash devices
  - CFI flashes with AMD command set
  - AT91SAM7 on-chip flash
  - STR7 on-chip flash
Support for additional core families
  - Intel XScale

---
OpenOCD
Additional JTAG Interfaces
USB + CPLD/FPGA
  - Universal solution
  - Latency critical
    - Offload logic from host to device
    - STAPL in hardware?
SBC + CPLD/FPGA
  - Ethernet, USB, ...
  - Task specific code runs on SBC
  - High-level protocol
    - GDB remote protocol
    - Boundary-Scan vector file player (SVF, STAPL)

---
Questions?
Thank your for your attention!
This project was supported by:
FuE-Programm
"Informations- und Kommunikationstechnik"
      http://www.iuk-bayern.de
      High-Tech Offensive Bayern (HTO)